## Slide 1: High Performance Processing of Streaming Data in the Cloud
AFOSR FA9550-13-1-0225: Cloud-Based Perception and Control of Sensor Nets and Robot Swarms
Geoffrey Fox, David Crandall,
Supun Kamburugamuve, Jangwon Lee, Jingya Wang January 27, 2016
gcf@indiana.edu
http://www.dsc.soic.indiana.edu/, http://spidal.org/ http://hpc-abds.org/kaleidoscope/
Department of Intelligent Systems Engineering
School of Informatics and Computing, Digital Science Center
Indiana University Bloomington

## Slide 2: Software Philosophy
We use the concept of HPC-ABDS High Performance Computing enhanced Apache Big Data Software Stack illustrated on next slide.
HPC-ABDS is a collection of 350 software systems used in either HPC or best practice Big Data applications. The latter include Apache, other open-source and commercial systems
HPC-ABDS helps ABDS by allowing HPC to add performance to ABDS software systems
HPC-ABDS helps HPC by bringing the rich functionality and software sustainability model of commercial and open source software. These bring a large community and expertise that is reasonably easy to find as it is broadly taught both in traditional courses and by community activities such as Meet up groups were for example:
  Apache Spark 107,000 meet-up members in 233 groups
  Hadoop 40,000 and installed in 32% of company data systems 2013
  Apache Storm 9,400 members
This talk focuses on Storm; its use and how one can add high performance

## Slide 3
Green implies HPC Integration
High Performance Computing Apache Big Data Software Stack

## Slide 4: IOTCloud
Device  Pub-SubStorm  Datastore  Data Analysis
Apache Storm provides scalable distributed system for processing data streams coming from devices in real time.
For example Storm layer can decide to store the data in cloud storage for further analysis or to send control data back to the devices
Evaluating Pub-Sub Systems ActiveMQ, RabbitMQ, Kafka, Kestrel
Turtlebot and Kinect

## Slide 5: 6 Forms of MapReduce cover “all” circumstances Describes different aspects - Problem - Machine - Software If these different aspects match, one gets good performance

## Slide 6: Cloud controlled Robot Data Pipeline
Message Brokers
RabbitMQ, Kafka
Gateway
Streaming Workflows
Apache Storm
Apache Storm comes from Twitter and supports Map-Dataflow-Streaming computing model
Key ideas: Pub-Sub, fault-tolerance (Zookeeper), Bolts, Spouts
Sending to
pub-sub
Sending to
Persisting
to storage
Streaming
workflow
A stream application with some tasks running in parallel
Multiple
streaming
workflows

## Slide 7: Simultaneous Localization & Mapping (SLAM)
Particles are distributed
in parallel tasks
Application
Build a map given the distance measurements from robot to objects around it and its pose
Streaming Workflow
Rao-Blackwellized particle filtering based algorithm for SLAM. Distribute the particles across parallel tasks and compute in parallel.
Map building happens periodically

## Slide 8: Parallel SLAM Simultaneous Localization and Mapping by Particle Filtering
Speedup

## Slide 9: Robot Latency Kafka & RabbitMQ
Kinect with
Turtlebot and RabbitMQ
RabbitMQ versus Kafka

## Slide 10: SLAM Latency variations for 4 or 20 way parallelism Jitter due to Application or System influences such as Network delays, Garbage collection and Scheduling of tasks
No Cut
Fluctuations decrease after Cut on #iterations per swarm member

## Slide 11: Fault Tolerance at Message Broker
RabbitMQ supports Queue replication and persistence to disk across nodes for fault tolerance
Can use a cluster of RabbitMQ brokers to achieve high availability and fault tolerance
Kafka stores the messages in disk and supports replication of topics across nodes for fault tolerance. Kafka's storage first approach may increase reliability but can introduce increased latency
Multiple Kafka brokers can be used to achieve high availability and fault tolerance

## Slide 12: Parallel Overheads SLAM Simultaneous Localization and Mapping: I/O and Garbage Collection

## Slide 13: Parallel Overheads SLAM Simultaneous Localization and Mapping: Load Imbalance Overhead

## Slide 14: Multi-Robot Collision Avoidance
Streaming Workflow
Information from robots
Runs in parallel
Second parallel Storm application
Velocity Obstacles (VOs) along with other constrains such as acceleration and max velocity limits,
Non-Holonomic constraints, for differential robots, and localization uncertainty.
NPC NPS measure parallelism
Control Latency
# Collisions versus number of robots

## Slide 15: Lessons from using Storm
We successfully parallelized Storm as core software of two robot planning applications
We needed to replace Kafka by RabbitMQ to improve performance
  Kafka had large variations in response time
We reduced Garbage Collection overheads
We see that we need to generalize Storm’s
  Map-Dataflow Streaming architecture to
  Map-Dataflow/Collective Streaming architecture
Now we use HPC-ABDS to improve Storm communication performance

## Slide 16: Bringing Optimal Communications to Storm
Both process based and thread based
parallelism is used
Worker and Task distribution of Storm
A worker hosts multiple tasks. B-1 is a task of component B and W-1 is a task of W
Communication links are between workers
These are multiplexed among the tasks
W-1
Worker
Node-1
B-1
W-3
Worker
W-2
W-5
Worker
Node-2
W-4
W-7
Worker
W-6
W-1
Worker
Node-1
B-1
W-3
Worker
W-2
W-5
Worker
Node-2
W-4
W-7
Worker
W-6

## Slide 17: Memory Mapped File based Communication
Inter process communications using shared memory for a single node
Multiple writer single reader design
A memory mapped file is created for each worker of a node
Create the file under /dev/shm
Writer breaks the message in to packets and puts them to file
Reader reads the packets and assemble the message
When a file becomes full move to another file
PS all of this “well known” BUT not deployed

## Slide 18: Optimized Broadcast Algorithms
Binary tree
  Workers arranged in a binary tree
Flat tree
  Broadcast from the origin to 1 worker in each node sequentially. This worker broadcast to other workers in the node sequentially
Bidirectional Rings
  Workers arranged in a line
  Starts two broadcasts from the origin and these traverse half of the line
All well known and we have used similar ideas of basic HPC-ABDS to improve MPI for machine learning (using Java)

## Slide 19: Java MPI performs better than Threads I 128 24 core Haswell nodes with Java Machine Learning Default MPI much worse than threads Optimized MPI using shared memory node-based messaging is much better than threads

## Slide 20: Java MPI performs better than Threads II 128 24 core Haswell nodes
200K Dataset Speedup

## Slide 21: Speedups show classic parallel computing structure with 48 node single core as “sequential” State of art dimension reduction routine Speedups improve as problem size increases 48 nodes, 1 core to 128 nodes 24 cores is potential speedup of 64

## Slide 22: Experimental Configuration
11 Node cluster
  1 Node – Nimbus & ZooKeeper
  1 Node – RabbitMQ
  1 Node – Client
  8 Nodes – Supervisors with 4 workers each
  Client sends messages with the current timestamp, the topology returns a response with the same time stamp. Latency = current time - timestamp
W-1
W-5
W-n
B-1
R-1
G-1
RabbitMQ
RabbitMQ
Client

## Slide 23: Original and new Storm Broadcast Algorithms
Speedup of latency with both TCP based and Shared Memory (for intra-node communication) based communications for different algorithms and sizes
Original
Binary Tree
Flat Tree
Bidirectional Ring

## Slide 24: Original and new Storm Broadcast Algorithms
Throughput with both TCP based and (for intra-node communication) Shared Memory based communications for different algorithms and sizes
Original
Binary Tree
Flat Tree
Bidirectional Ring

## Slide 25: Future Work
Memory mapped communications require continuous polling by a thread. If this tread does the processing of the message, the polling overhead can be reduced.
Scheduling of tasks should take the communications in to account
The current processing model has multiple threads processing a message at different stages. Reduce the number of threads to achieve predictable performance
Improve the packet structure to reduce the overhead
Compare with related Java MPI technology
Add additional collectives to those supported by Storm

## Slide 26: Conclusions on initial HPC-ABDS use in Apache Storm
Apache Storm worked well with performance enhancements
For Binary tree performed the best
Algorithms reduces the network traffic
Shared memory communications reduce the latency further
Memory mapped file communications improve performance

## Slide 27: Thank You
References
  Our software https://github.com/iotcloud
  Apache Storm http://storm.apache.org/
  We will donate software to Storm
  SLAM paper http://dsc.soic.indiana.edu/publications/SLAM_In_the_cloud.pdf
  Collision Avoidance paper http://goo.gl/xdB8LZ

## Slide 28: Deep learning in interactive applications
State of the art deep learning-based object detectors can recognize among hundreds of object classes
This capability would be very useful for mobile devices, including robots
But, compute requirements are enormous
  Model for a single object has millions, billions of parameters
  Classification requires ~20 sec/image on a high end CPU,
  and ~2 sec/image on a high-end GPU
Use Regions with Convolutional Neural Networks CNNs (R-CNNs) trained on ImageNet (obviously not best)

## Slide 29: Recognition on an aerial drone
Scenario: a drone needs to navigate through cluttered environment to locate a particular object
Major challenges
  Communications link with limited bandwidth
  Long, unknown latencies for network and cloud
  Real-time decisions needed for stability control

## Slide 31: Hierarchical Recognition Pipeline
Images @ 10Hz
Detected object location
PID Control
Servo
commands
Images @ 60Hz
High-level navigation commands
Images @ <1Hz
Recognized objects
Low-level feature extraction for stability control
Landmark recognition, object detection
Deep CNN-based object recognition
On drone
Near drone
Far away

## Slide 34
Regions with CNNs (R-CNNs)

## Slide 35: Spare SLAM Slides

## Slide 36
IoTCloud uses Zookeeper, Storm, Hbase, RabbitMQ for robot cloud control
Focus on high performance (parallel) control functions
Guaranteed real time response
Parallel
simultaneous localization and mapping
(SLAM) in the cloud

## Slide 37: Latency with Kafka Note change in scales for latency and message size
Latency with RabbitMQ
Different Message sizes in bytes

## Slide 38: Robot Latency Kafka & RabbitMQ
Kinect with
Turtlebot and RabbitMQ
RabbitMQ versus Kafka

## Slide 39: Parallel SLAM Simultaneous Localization and Mapping by Particle Filtering

## Slide 40: Spare High Performance Storm Slides

## Slide 41: Memory Mapped Communication
write | Packet 1 | Packet 2 | Packet 3 | 
Writer 01
Writer 02
Write
Write
Obtain the write location atomically and increment
Shared File
Reader
Read packet by packet sequentially
Use a new file when the file size is reached
Reader deletes the files after it reads them fully
ID | No of Packets | Packet No | Dest Task | Content Length | Source Task | Stream Length | Stream | Content
16 | 4 | 4 | 4 | 4 | 4 | 4 |  | 
Bytes
Fields
Packet Structure

## Slide 42: Default Broadcast
W-1
Worker
Node-1
B-1
W-3
Worker
W-2
W-5
Worker
Node-2
W-4
W-7
Worker
W-6
B-1 wants to broadcast a message to W, it sends 6 messages through 3 TCP communication channels and send 1 message to W-1 via shared memory

## Slide 43: Memory Mapped Communication
No significant difference
because we are using all
the workers in the cluster beyond 30 workers capacity
A topology with pipeline going through all the workers
Non Optimized Time

## Slide 44: Spare Parallel Tweet Clustering with Storm Slides

## Slide 45: Parallel Tweet Clustering with Storm
Judy Qiu, Emilio Ferrara and Xiaoming Gao
Storm Bolts coordinated by ActiveMQ to synchronize parallel cluster center updates – add loops to Storm
2 million streaming tweets processed in 40 minutes; 35,000 clusters
Sequential
Parallel – eventually 10,000 bolts

## Slide 46: Parallel Tweet Clustering with Storm
Speedup on up to 96 bolts on two clusters Moe and Madrid
Red curve is old algorithm;
green and blue new algorithm
Full Twitter – 1000 way parallelism
Full Everything – 10,000 way parallelism