## Slide 1
Versatile HPC: Comet Virtual Clusters for the Long Tail of Science SC17 Denver Colorado
Comet Virtualization Team: Trevor Cooper, Dmitry Mishin, Christopher Irving, Gregor von Laszewski (IU) Fugang Wang (IU), Geoffrey C. Fox (IU), Phil Papadopoulos

## Slide 2: Motivation for Virtual Clusters
Goal: Provide near bare metal HPC performance and management experience for groups that can manage their own clusters.
OS and software requirements are diversifying. Growing number of user communities that can’t work in traditional HPC software environment.
Communities that have expertise and ability to utilize large clusters but need hardware.
Institutions that have bursty or intermittent need for computational resources.

## Slide 3: Key for Performance: Single Root I/O Virtualization (SR-IOV)
Problem: Virtualization generally has resulted in significant I/O performance degradation (e.g., excessive DMA interrupts)
Solution: SR-IOV and Mellanox ConnectX-3 InfiniBand host channel adapters
  One physical function  multiple virtual functions, each light weight but with its own DMA streams, memory space, interrupts
  Allows DMA to bypass hypervisor to VMs
SRIOV enables virtual HPC cluster w/ near-native InfiniBand latency/bandwidth and minimal overhead
Notes: Virtualization  flexibility to run compute appliances:
  run complex workflows with very specific application environments
  tightly integrated, custom combinations of software: OS, libraries, and applications code/versions
Performance loss due to virtualized environments has been the major barrier
  Virtualizing IO (DMAs) can cause excessive CPU interrupts
  High-performance interconnect (InfiniBand) performance suffers
Solution: Single Root I/O Virtualization (SR-IOV) within Mellanox ConnectX-3 InfiniBand HCAs
  provides technology for low-overhead DMA to virtual machines
  non-proprietary industry standard: provides virtual functions for PCIe devices

## Slide 4: User-Customized HPC 1:1 physical-to-virtual compute node
Frontend
Virtual Frontend
Hosting
Disk Image Vault
Compute
Compute
Compute
Compute
Compute
Compute
Compute
Compute
Compute
public network
private
Virtual
Compute
Virtual
Compute
Virtual
Compute
private
Virtual
Compute
Virtual
Compute
Virtual
Compute
private
physical
virtual
virtual
Virtual
Frontend
Virtual
Frontend

## Slide 5: User Perspective User is a system administrator –we give them their own HPC cluster
Nucleus
Persistent virtual front end
API
Request nodes
Console & power
Scheduling
Storage management
Coordinating network changes
VM launch & shutdown
Idle disk images
Active virtual compute nodes
Disk images
Attached and synchronized

## Slide 6: Accessing Virtual Cluster Capabilities
REST API
Command line interface
Command shell for scripting
Console Access
(Portal)
User does NOT see: Rocks, Slurm, etc.
Reference: https://github.com/cloudmesh/client
https://github.com/cloudmesh/comet
hybrid clouds OpenStack, (EC2, AWS, Azure);

## Slide 7: Cloudmesh supports Continuous Improvement

## Slide 8: Layered Architecture

## Slide 9: Benefits
On same machine
  MPI
  Virtual Cluster
  Containers
Allows reuse of technologies developed by local staff
  Replicate your cluster on comet
  Leverage local account management, e.g. if you have a large class you could use the existing account system simplifying access
  Software stacks you developed