## Slide 1: Streaming Applications for Robots with Real Time QoS
Oct-28-2015
Supun Kamburugamuve
Indiana University

## Slide 2: Research at IU Digital Science Center
Offloading robotic algorithms to servers
  Save power
  Increase mobility
We consider expensive computations
Latency and Jitter are the most important performance characteristics
Need parallel computations to reduce latency
  Both at robot level and across robots
We work with mostly constant rate data streams

## Slide 3: Data pipeline
Message Brokers
RabbitMQ, Kafka
Gateway
Sending to
pub-sub
Sending to
Persisting
to storage
Streaming
workflow
A stream application with some tasks running in parallel
Multiple
streaming
workflows
Streaming Workflows
Apache Storm
Hosted in FutureSystems OpenStack VMs which are accessible through IU network
End to end delays without any processing is less than 10ms

## Slide 4: Simultaneous Localization & Mapping (SLAM)
Particles are distributed
in parallel tasks
Build a map given the distance measurements from robot to objects around it and its pose
Streaming Workflow
Parallel Speedup
Rao-Blackwellized particle filtering based algorithm for SLAM. Distribute the particles across parallel tasks and compute in parallel.
Map building happens periodically

## Slide 5: Multi-Robot Collision Avoidance
Streaming Workflow
Information from robots
Runs in parallel
Velocity Obstacles (VOs) along with other constrains such as acceleration and max velocity limits, Non-Holonomic constraints, for differential robots, and localization uncertainty.
Control Latency
Collisions with number of robots
5 Compute Velocity Tasks

## Slide 6: Jitter
No Cut
Fluctuations decrease after Cut on #iterations per swarm member
Nature of application
System level influences
    Network
    Garbage collection
    Scheduling of tasks
    Virtualization
SLAM Latency variations

## Slide 7: Bringing Optimal Communications to Storm
Optimized
20 or 50 tasks
Original
50 Tasks
Original
20 Tasks
Memory mapped files for intra-node communications
Both process based and thread based
parallelism is used
Chart: Message size in bytes
| 10000 | 20000 | 40000 | 60000 | 80000 | 100000 | 120000 | 140000 | 160000 | 180000
50-Naïve | 6 | 10 | 19 | 27 | 35 | 43 | 51 | 59 | 68 | 75
50-Tree Broadcast | 4 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
20-Naïve | 4 | 6 | 9 | 13 | 17 | 21 | 25 | 32 | 38 | 43
20-Tree Broadcast | 3 | 4 | 6 | 8 | 10 | 12 | 14 | 17 | 19 | 21
Worker and Task distribution of Storm
Broadcast takes advantage of task locality
Binary tree broadcast

## Slide 8: Summary of Challenges
Maintaining the latency within reasonable bounds
  Scheduling for predictable performance
  Duplicate computations to remove random increases
Higher level abstractions for complex streaming applications
  Storm API is low level (MPI like, fast) and Spark Streaming is high level (Slow).
Scaling to multiple data sources

## Slide 9: Thank You
References
  Projects https://github.com/iotcloud
  Apache Storm http://storm.apache.org/
  SLAM http://dsc.soic.indiana.edu/publications/SLAM_In_the_cloud.pdf
  Collision Avoidance http://goo.gl/xdB8LZ